1. Power from 12V
   Verify power LED is lit
   Loosen GND and track screws while powering up

  Figure 1
2. Factory Reset
3. Attach 12Ω resistor to TRACK terminals
   Monitor voltage and current
   Verify both track LEDs are lit
4. Enter Diagnostics menu
   Short each sensor input to GND, verifying response on display
5. Place in 6x8 anti-tatic bag (Figure 1)
   Tape closed on back
  Figure 2
6. Place face down on folded packing paper (Figure 2)
7. Wrap and fold paper loosely over front (Figure 3)
8. Put layer of crinkle paper in box
9. Place control unit in back of box, face down, with power supply toward front (Figure 4)
  Figure 3
10. Place selected IR sensor on top (Figure 5)
11. Insert manual and close box
12. Label box in middle of top lid, small piece of tape to hold closed

Figure 4
Figure 5