1. Power from 12V
   Verify power LED is lit
   Loosen GND and track screws while powering up

  Figure 1
2. Factory Reset
3. Attach 12Ω resistor to TRACK terminals
   Monitor voltage and current
   Verify both track LEDs are lit
4. Enter Diagnostics menu
   Short each sensor input to GND, verifying response on display
5. Place in 6x8 anti-tatic bag (Figure 1)
   Tape closed on back
6. Place facedown with power supply on WrapPak (Figure 2)

  Figure 2
7. Wrap and fold paper over back side (Figure 3)

  Figure 3

  Figure 4
8. Place in box
   Power supply toward front and folded paper down (Figure 4)
9. Place selected IR sensor on top (Figure 5)
10. Put manual down front and fold over (Figure 6)
11. Close & label box

Figure 5

Figure 6